## Slide 1
CHANGELOOP
SANKALP 2026 · STUDENTS TRACK · CLIMATE AND WATER
In a zero-discharge dyehouse, the evaporator's fuel bill is set by how much salt goes into the dye bath — not by how much water comes out.
A scheduling choice this morning sets how much fuel the evaporator burns tonight. India already recycles its industrial water under Zero Liquid Discharge. Nobody has costed the energy it takes to keep doing so — and that cost is decided upstream, by a planner who never sees the evaporator.
130 million L/day
ALREADY RECYCLED IN ONE CLUSTER
+25 to 30%
WHAT THAT COMPLIANCE COSTS
700 units
SHUT BY COURT ORDER IN 2011
Notes: Say the title sentence out loud, then pause. In February 2011 the Madras High Court shut around 700 dyeing units in Tirupur, on a contempt petition from the farmers whose river they had been discharging into. Exports fell about a thousand crore in a quarter. The cluster rebuilt and now recycles 130 million litres a day, which worked, and raised operating costs 25 to 30 percent. Nobody has costed the fuel. Job-loss estimates for 2011 range from 15,000 by the exporters association to 200,000 in press reporting, so do not quote a single figure - say tens of thousands if asked.

## Slide 2: ChangeLoop in six boxes
ON ONE PAGE
Resource decision intelligence for Indian textile clusters operating under a court-mandated Zero Liquid Discharge regime.
PROBLEM
Compliance is solved. Its energy bill is not.
ZLD recycles the cluster’s water and raised operating costs 25 to 30 percent. Pollution-board data puts the charge at ₹150–220 per kilolitre against ₹45 for river water — and ₹375–450 at under-used plants.
INSIGHT
In a closed loop, salt is water.
Reject volume equals salt mass over the RO ceiling, so evaporator steam tracks salt, not water. Cut water 20 percent at constant salt and the energy moves 0.0 percent.
SOLUTION
Price the evaporator into the schedule.
Two human-gated decisions: which plan to run, and when wash-off is finished. 480 candidates scored on water, salt, steam, carbon, cost and ship dates at once.
INNOVATION
Two levers that pull apart.
Counter-current rinsing cuts water but not salt. Low-electrolyte chemistry cuts salt but not water. A water-only tool picks the wrong one with full confidence.
IMPACT
The water lever moves the envelope by nothing.
Doing nothing runs at 132.3 percent of a real machine-shift allowance. Counter-current rinsing runs at 132.3 percent too — identical. Only the salt lever gets inside, at 82.1 percent.
EVIDENCE
Checked against published plant data.
Fed the 18,340 mg/L inlet CPCB measured at a Tirupur unit, the model predicts 30.6 percent reject — inside the 20–30 operators report. 21 of 25 coefficients sourced, zero measured.
The ask: one dyeing unit or effluent plant willing to share two instrument readings — steam flow to the evaporator, and reject conductivity. Everything else is already sourced from CPCB, the CEA, TNERC and pollution-board data. Those two are all that separate a validated model from a measured one.
Notes: If a judge reads only one slide, this is it. Problem, insight, solution, innovation, impact and evidence, each in three lines, with the ask at the foot. Everything that follows is corroboration.

## Slide 3: A seasonal river and a bill nobody costed
THE PROBLEM
The Noyyal has no dry-weather flow to dilute effluent, so discharge was ruled out entirely and Zero Liquid Discharge was imposed on the cluster.
Farmers lost the water first
The litigation was brought by the Noyyal River Ayacutdars Association — a farmers’ body. The Orathupalayam dam, built to irrigate about 20,000 hectares, became a repository of polluted water.
Compliance became survival
Zero Liquid Discharge now recycles most of the cluster’s water. It also raised unit operating costs 25 to 30 percent, in a cluster dominated by MSMEs that cannot absorb it.
The gap is between systems
The dyehouse ERP plans lots. The treatment plant treats whatever arrives. The regulator monitors the outfall. None of them talk, and often they are different companies.
Reported figures. Sources listed in the appendix and in the product’s own claim register.
Notes: Three points. The downstream victims were farmers, and they are the ones who went to court. Compliance worked but it is expensive, and these are small units. And the reason the cost is not managed is that the decision and the consequence live in different organisations.

## Slide 4: Recovery is solved. Paying for it is not
WHERE THE REAL COST SITS
Recycled water costs two to five times the freshwater it replaces, because somebody had to boil the reject dry to make it.
WHAT IT COSTS | FRESH | RECYCLED
Water, per kilolitre | ₹30 to 60 | ₹120 to 150
Operating cost impact of ZLD | — | +25 to 30%
Cost of dyed fabric | — | +12 to 15%
With salt and water recovery | — | about +5%
The industry already names the lever
The reported route from a 12 to 15 percent fabric cost penalty down to about 5 percent is salt and water recovery.
So the question is not whether salt matters. It is who decides how much salt enters the water in the first place — and nobody is doing that.
Avoiding a litre of demand is worth more than recovering a litre of effluent. That is why ChangeLoop acts upstream.
Notes: This is the slide that reframes the problem. Everyone assumes the water problem is recovery. Recovery is done. The marginal litre in a closed loop comes from the recycle train at 120 to 150 rupees, not the borewell at 30 to 60. So avoiding demand is worth far more than recovering waste.

## Slide 5: In a zero-liquid-discharge plant, salt is water
THE INSIGHT
Salt is conserved. Reverse osmosis can only concentrate it to a ceiling before scaling stops it. So by mass conservation:
V_reject = M_salt / C_reject_max
Reject volume — and therefore evaporator steam, fuel and CO₂ — is set by SALT MASS, not by water volume.
COMPUTED LIVE IN THE PRODUCT
Cut water 20%, salt unchanged
0.0%
evaporator energy does not move
Cut salt 20%, water unchanged
-20.0%
evaporator energy falls proportionally
And where it stops
Below a crossover the membrane hydraulic floor takes over and cutting salt buys nothing further. A product claiming that cutting salt always wins would be wrong, so the engine reports which constraint binds on every stream.
Cutting water without cutting salt does not cut evaporator energy. Because the loop is closed, freshwater makeup equals exactly what was evaporated — so freshwater, evaporator load and carbon are the same number.
Notes: This is the slide the pitch turns on. The arithmetic is exact, it is mass conservation, and the product computes it live. Cut water twenty percent at constant salt and evaporator energy moves zero point zero. Cut salt twenty percent and it falls twenty. A water dashboard cannot see this. One caveat we state openly: below a crossover the membrane floor takes over and salt reduction stops paying, and the engine reports which constraint binds.

## Slide 6: Tonight’s evaporator bill, priced this morning
THE SOLUTION
A decision layer, not a dashboard. It scores every feasible plan on the whole downstream consequence.
10,863 L freshwater makeup
Dyehouse
40,773 L demand
RO
73.4% recovery
Permeate reused
29,910 L
Reject evaporated
10,863 L
Steam and CO₂
2,043 kWh th
returns to the process
Band thickness is volume. The loop that returns is fat; the freshwater top-up is thin — and it is exactly as thick as what the evaporator destroyed.
Two decisions, each gated by a named human
01
Which plan to run. Lot order plus process strategy, scored on every consequence at once.
02
When wash-off is finished. Releasing early on unfixed dye forces a re-process that costs more than it saved.
Notes: We are not another monitoring dashboard. We sit at the moment of decision. Two decisions, both human-gated. The system has no control authority at all, which is deliberate: a tool that can stop a line will never be allowed near one.

## Slide 7: Two levers that pull in opposite directions
THE INNOVATION
This is why a joint objective is required, and why a water-only tool picks the wrong lever with full confidence.
PROCESS LEVER | CUTS WATER | CUTS SALT | CUTS EVAPORATOR ENERGY
Counter-current rinse cascade | yes, ~35% | no | barely — same salt, less water
Low-electrolyte dye chemistry | no | yes, ~45% | yes, proportionally
What we claim, narrowly
01
The downstream consequence inside the objective. Evaporator steam, boiler carbon and treatment cost, scored per candidate plan.
02
Salt-mass accounting as the energy driver. Acting on it inverts the normal advice.
03
Hard constraints as feasibility, not penalty. A saving cannot buy its way out of a firm ship date.
What we explicitly do not claim
Ascending shade sequencing is standard dyehouse practice. Counter-current rinsing is established best available technique. Low-electrolyte reactive dyes are a commercial product. Zero Liquid Discharge, reverse osmosis and multi-effect evaporation are all existing industry. None of these is our invention, and the product says so on screen.
Notes: The honest version of a novelty claim. Every component is existing industry and we name them. What is new is the coupling: putting the evaporator consequence inside the scheduling objective, and enforcing constraints as feasibility. The next slide shows what that coupling is worth, measured by ablating our own system.

## Slide 8: It refuses the plan that saves the most water
THE PRODUCT, RUNNING
480 candidates enumerated exhaustively — 120 lot orders against 4 process strategies — so the optimum is proven, not approximated.
PLAN | FRESHWATER | SALT | EVAPORATOR | CO₂e | COST | LATE
A No intervention | 11,907 L | 714 kg | 2,239 kWh | 3,063 kg | ₹33,897 | 0.0 h
B ChangeLoop, recommended | 11,187 L | 671 kg | 2,104 kWh | 2,305 kg | ₹26,038 | 0.0 h
C Freshwater minimum — REFUSED | 5,889 L | 353 kg | 1,108 kWh | 2,194 kg | ₹32,781 | 2.6 h
Why C is refused
Option C saves almost half the freshwater and ChangeLoop will not recommend it, because it breaches a firm buyer ship date by 2.6 hours.
That refusal is the product working. A water tool that misses a shipment gets switched off in a week.
Every number on this slide is produced by the engine and traceable
Click any figure in the interface and it opens its formula, its upstream chain, and every coefficient with that coefficient’s unit, derivation and evidence class. 8 accounting invariants run on every read of the ledger — water balance, salt balance, no double counting, no credit for an unapproved decision. If one fails, the figure is not displayed.
Notes: Walk the table left to right, then land hard on Option C. This is the credibility moment: we show the plan that would have given us the best headline, and we refuse it on camera. Then the traceability point: every number opens its own derivation.

## Slide 9: The water lever alone does not get you compliant
THE OPERATIONAL MANDATE
Judged against a real per-machine-shift abstraction allocation: 72,000 L/day site allowance / (4 machines x 2 shifts) = 9,000 L per machine-shift
Do nothing
11,907 L
132.3%
breaches at 14:00
Resequence + counter-current (water lever)
11,907 L
132.3%
still breaches at 14:00
Resequence + combined (buys the salt lever)
7,387 L
82.1%
inside the allocation
allocation
Resequencing and reusing rinse water cuts 720 litres and still misses the allocation by a quarter. Only cutting the salt gets the shift inside it. This is the thesis as an operating instruction — and it fell out of the model, not out of a slide.
Notes: If there is one slide to leave with the jury, this is it. Same queue, three plans, one allocation. The intuitive answer, reusing rinse water, still breaches. The counter-intuitive one, buying low-salt chemistry, is the only one that complies. We did not design this result; the forecast module produced it when we judged the projection against a real allocation instead of a whole-site daily figure.

## Slide 10: Modest, internally consistent, and traceable
THE IMPACT
One shift, one machine, five lots. Everything here is MODELLED — nothing in the prototype is metered, and a test enforces that.
1,044 L
FRESHWATER AVOIDED
11,570 L-eq stress weighted, in a basin
with no dry-weather flow
62.7 kg
SALT LOAD AVOIDED
this is what sets the
evaporator duty
196 kWh
EVAPORATOR STEAM AVOIDED
thermal, at the
common treatment plant
926 kg
CO₂E AVOIDED, DOWN 30.2%
₹9,709 saved per shift,
down 28.6%
At cluster scale
75.0 million litres of freshwater, 4,500 tonnes of salt, 14,106 MWh of evaporator steam and 6,376 tonnes CO₂e a year, across 400 units on one common effluent plant.
And this is a projection, not a result
It assumes every unit resembles the modelled one and that every recommendation is approved. Neither has been tested. The interface labels it PROJECTED and we will not quote it as achieved impact.
Notes: Our per-shift numbers are modest and we present them that way deliberately. A modest figure that survives scrutiny is worth more to us than an impressive one we cannot defend. Note freshwater falls 8.8% while cost falls 28.6% and carbon 30.2%, because basin draw tracks salt while cost and carbon also pick up the rinse-water heat.

## Slide 11: We remove our own layers and publish what breaks
PROOF, NOT ASSERTION
Reproducible from the product’s own API. At today’s prices, the layers that bind are the salt model and the ship-date rules. Price water scarcity and a scheduler that optimises dyehouse water alone captures 13 percent of the available benefit.
VARIANT | FRESHWATER REPORTED | VS FULL | BREACH | VERDICT
Full ChangeLoop | 720 L | 100.0% | undefined | baseline for comparison
Without downstream ZLD coupling | 720 L | 100.0% | undefined | no effect at this site
Without the salt-mass model (water-only ZLD) | 2,343 L | 325.4% | undefined | loses most of the benefit
Without basin stress weighting | 720 L | 100.0% | undefined | no effect at this site
Without hard-constraint enforcement | 1,200 L | 166.7% | undefined | loses most of the benefit
Two variants report MORE than is really there
Over-reporting is their defect, not an advantage. A water-only ZLD model mis-states how much freshwater a plan really avoids. We label it as such in the product.
And one of our layers earns nothing here
Basin stress weighting does not change the answer at a single site. It only earns its place for multi-site prioritisation, and our own study says so rather than pretending otherwise.
Notes: This is the slide that separates us from a demo. We ablate our own architecture and publish the parts that do not earn their place, including a layer that contributes nothing at one site and two variants that lie upward. A jury that sees a team marking its own homework honestly will trust the rest of the numbers.

## Slide 12: The cluster is the unit. The CETP is the channel
WHO PAYS, AND HOW WE WOULD KNOW IT WORKED
ROLE | WHY THEY ENGAGE
Unit owner | Buys it. Steam and salt are cash to an MSME.
Production planner | Uses it. Will not accept a missed ship date.
Quality supervisor | Holds the veto on wash-off release.
Common effluent plant | The channel. One integration reaches hundreds of units, and a lower inlet salt load is its own gain.
Buyer or brand | Pulls demand, for Scope 3 water and carbon evidence.
Priced per machine per year, plus one-off integration
Machines, not sites: it scales with the decisions the product actually touches. The business-case screen refuses to compute a return until the site enters its own tariffs — a projection built on a vendor’s assumptions is not a business case.
Six-phase pilot, designed to answer one question
Did ChangeLoop cause the reduction, or would it have happened anyway?
1
Baseline metering measure before we influence anything
wk 1–4
2
Shadow mode we recommend, nobody acts
wk 5–8
3
Advisory with approval alternate weeks on and off
wk 9–16
4
Wash-off release trial every released lot fastness-tested
wk 17–24
5
Chemistry decision once steam cost is measured
wk 25–32
6
Cluster rollout second and third unit
wk 33+
A single wash-fastness failure stops the trial. Until phase 3 completes, every figure we show is MODELLED and we will not call it a result.
Notes: Commercial honesty. The hardest objection is that an MSME will not pay for a modelled saving, so the answer is shadow mode: four weeks of recommending while nobody acts, then charge against a measured baseline. And the effluent plant is the channel because its incentive is already aligned.

## Slide 13: A working system you can run and attack
NOT A MOCK-UP
Python standard library only. No dependencies, no build step, no account. One command and the whole decision loop is live.
01
Observe
order book and
basin allocation
›
02
Project
causal forecast
vs the envelope
›
03
Optimise
480 candidates,
optimum proven
›
04
Decide
a named human
approves or refuses
›
05
Gate
fail-closed
wash-off release
›
06
Account
mass balance and
8 invariants
›
07
Prove
tamper-evident
ledger and export
190
AUTOMATED TESTS
engine, published-data validation,
concurrency, safety and tamper
34
API ENDPOINTS
every figure on screen is
server-computed and traceable
8
OPERATING SCREENS
command, forecast, decisions,
water, impact, evidence, audit
5
FAULT MODES TESTED
each must force lockout
and credit exactly zero
0
MEASURED COEFFICIENTS
enforced by a test, because
nothing here is metered yet
Attack it live: inject a probe fault and release is refused at the gate and again at the API, the refusal is written to the ledger, and the credited saving stays at zero. Edit a ledger row by hand and the chain names exactly which record broke.
Notes: This slide kills the doubt that the deck is the whole project. It runs, it is tested, and it is built to be attacked on camera. Zero measured coefficients is deliberate and test-enforced: better to show a zero than imply data we do not have.

## Slide 14: Fed real plant data, it predicts what real plants report
HOW WE CHECKED A MODEL WITH NO METERS
We have measured nothing, and we say so on every screen. But a model with no measurements can still be falsified — by asking whether its OUTPUTS land where real plants actually sit.
FACT ONE · MEASURED BY CPCB
18,340 mg/L of dissolved solids entering the evaporator at an assessed Tirupur dyeing unit.
FACT TWO · REPORTED BY OPERATORS
RO reject runs at 20 to 30 percent of inlet volume across Indian textile ZLD plants.
Different sources. Neither one is an input to our engine. So we feed it the first and check whether it predicts the second.
INLET TDS FED IN | WHAT THAT NUMBER IS | MODEL PREDICTS | VERDICT
12,000 mg/L | Lower end of observed CETP inlet strength | 20% | inside 20–30%
15,000 mg/L | Midpoint of observed CETP inlet strength | 25% | inside 20–30%
18,340 mg/L | TDS measured by CPCB entering evaporation at an assessed Tirupur unit | 30.6% | inside 20–30%
Nothing is tuned to make this work. The only inputs are conservation of salt mass and the 60,000 mg/L concentration ceiling. The published band is reproduced from floor to ceiling, and a test fails the build if it stops being.
21/25
COEFFICIENTS SOURCED
CPCB, CEA, TNERC,
pollution board, EU BAT
0
MEASURED
and we will not pretend
otherwise to win a prize
This is cross-validation against published operating data. It is not measurement, and we never call it that.
Notes: This is the slide that answers the hardest fair objection: you have no data. Correct. But watch what happens when we feed the model a number CPCB measured at a real unit and compare its output to what operators independently report. Twelve thousand gives exactly twenty percent, the floor of the band. Eighteen thousand three hundred and forty, CPCB's own measured inlet, gives thirty point six, the ceiling. The band is reproduced end to end and nothing was tuned to do it. Then be the first to say the limit out loud: this is validation, not measurement, and the ask on slide two is the two readings that would change that.

## Slide 15: Built, tested and adversarially reviewed
THE TEAM
Shorya Ashish Mittal
TEAM LEADER
Engine, water accounting and interface
What exists today
A working engine and interface, dependency-free. 190 automated tests across 7 suites: the engine, cross-validation against published plant data, registry concurrency, safety interlocks over five fault modes, a determinism check, and a tamper test that breaks the ledger chain on purpose to prove it detects it. Evidence discipline: 17 published, 4 derived, 4 assumed and zero measured coefficients — enforced by a test.
Our biggest weakness, stated first
We have not yet spoken to a dyehouse. Everything is modelled from public information, the basin weighting is a disclosed placeholder, and the optimiser handles one machine rather than a mill. Phase 1 of the pilot exists to replace our assumptions with their measurements — and some of our conclusions will change when it does.
What we are asking for: one Tirupur dyeing unit or CETP willing to share two instrument readings: steam flow to the evaporator, and reject conductivity. Everything else is already sourced from CPCB, the CEA, TNERC and pollution-board data — those two are all that separate a validated model from a measured one.
Zero Liquid Discharge gave India back its water. Nobody costed the fuel it takes to keep it — and that cost is decided by a scheduling choice nobody connects to it.
Notes: Close on the team, then the weakness, then the hook. Naming the weakness before the jury does is the strongest thing we can do here: it tells them the rest of the numbers were assembled by people who look for their own errors. Then the memory line.